## Slide 1
Chapter 4 First-Order Circuits
3. Zero-input response，Zero-state response and complete response
key points
2. Equation and initial conditions of dynamic circuits
1. Capatiors and Inductors

## Slide 2
4.1.1 Capacitors
1. Definition
Capacitor
A capacitor is a passive element designed to store energy in its electrical field.
q
u
q-u
relationship
4.1 Dynamic element
A capacitor consists of two conducting plates separated by an insulator (or dielectric).

## Slide 3
The amount of charge stored on the capacitor plate, represented by q, is proportional to the applied voltage u, then q ~ u curve is a line that goes through the origin.
Circuit symbol
2. Linear capacitor
C
＋
－
u
+q
-q
C is known as the capacitance of the capacitor.
The unit of capacitance is the farad (F).
q
u
O
α
Unit
Capacitor have values in the picofarad (pF) to microfarad(μF) range.

## Slide 4
The current-voltage relationship for a capacitor
C
＋
－
u
i
the associated reference direction
Differential expression of current-voltage relationship for a capacitor
(1) The value of i depends on the change rate of u and has nothing to do with the value of u. A capacitor is a dynamic element;
(2) When the voltage across a capacitor is not changing with time (i.e., dc voltage), the current through the capacitor is zero. A capacitor is an open circuit to dc;
(3) In the actual circuit, the current through a capacitor is finite, and the voltage on the capacitor must be continuous and cannot change abruptly.

## Slide 5
The capacitor voltage depends on the past history of the capacitor current. Hence, the capacitor has memory property.
（1）When u and i adopt non-associated reference direction, a negative sign is added before the above formulas;
（2）u(t0) is called the initial voltage value of capacitor，which reflects the energy storage condition at the initial time of capacitor, also known as the initial state.
Integral expression
Thus:
Note:

## Slide 6
3. The power and energy
Power
Thus:
The ideal capacitor does not dissipate energy. It taks power from the circuit when storing energy in its field and returns previously stored energy when delivering power to the circuit.
Therefore, capacitor is a passive component and an energy storage component, which does not consume energy.
Associate reference direction
When the capacitance is discharged，u>0，d u/d t <0，so i<0, q , p<0, capacitor deliver power.
When the capacitor is charged， u>0，d u/d t >0，so i>0, q , p>0, capacitor absorbe power.

## Slide 7
Energy storage by capacitors is only dependent on voltage, and the voltage of a capacitor cannot change abruptly.
The change of energy stored by capacitor from t0 to t ：
The energy stored in the capacitor
if
We note that ,because the capacitor was uncharged at t =-∞.

## Slide 8
4.1.2 Inductors
i (t)
+
-
u (t)
Inductance coil
The metal wire is wound on a frame to form a practical inductor. When the current flows through the coil, it will produce magnetic flux.
Ψ(t)＝N Φ(t)
1. Definition
Inductors
An inductor is a passive element designed to store energy in its magnetic field.
i
Ψ
Wb-A
relationship

## Slide 9
At any time, the current i flowing through the inductor is proportional to its flux Ψ. The characteristic of Ψ~ i relationship of a linear inductor is a straight line passing through the origin.
Circuit symbol
2. Linear inductor
L is the inductance of the inductor.
The unit of inductance is the henry (H).( or μH, mH)
Ψ
i
O
α
+
-
u (t)
i
L
Unit

## Slide 10
Voltage-current relationship of inductor
associate reference direction
Differential expression
(1) The voltage value of inductor is only dependent on the change rate of i, and has nothing to do with the value of i. inductor is a dynamic element;
(2) The voltage across an inductor is zero when the current is constant. Thus, the inductor acts like a short circuit to dc;
(3)In the actual circuit, the voltage value of inductor is finite. The current flowing through an inductor cannot change abtuptly, and it must be a continuous function of time.
+
-
u (t)
i
L

## Slide 11
The inductor current depends on the past history of the inductor voltage. Hence, the inductor has memory property.
(1) When u and i use the non-associate direction, the above differential and integral expressions should be preceded by a minus sign;
(2) In the above formula, i(t0) is called the initial current value of the inductor, which reflects the energy storage state at the initial time, also known as the initial state.
Integral expression
Thus:
Note:

## Slide 12
3. The power and energy
Power
Thus:
In a period of time, the inductor can absorb the energy from the external supply and convert it into magnetic energy for storage. In another period of time, it releases the energy back to the circuit. Therefore, the inductor is a passive component and an energy storage component, which does not consume energy.
associate reference direction
When the current increases, i >0, d i/d t>0, so u>0, p>0, inductor absorbed power.
When the current decreases, i>0, d i/d t<0, so u<0, p<0, inductor deliver power.

## Slide 13
(1)The energy of the inductor is only related to the current value at that time, and the inductor current cannot change abruptly, which reflects the energy cannot change abruptly;
(2) The energy stored in the inductor must be greater than or equal to zero.
The energy changes from t0 to t：
Energy storage of inductors
Thus:
if

## Slide 14
Comparison of capacitors and inductor
(1) The form of the equation is similar；
Conclusion:
Capacitor
Inductor
Variable
current i
flux Ψ
Equation
voltage u
charge q
(2) If u-i, q- , C-L and i-u, are interchanged, the equation of inductor can be obtained from the equation of capacitor ；
(3) C and L are called dual elements.

## Slide 15
4.1.3 Series and parallel capacitors and inductors
1. Capacitors
Capacitors in series combine
......

## Slide 17
Capacitors in parallel combine

## Slide 18
2. Inductors
Inductors in series combine

## Slide 19
Inductors in parallel combine

## Slide 20
The circuit with dynamic element capacitance and inductance is called dynamic circuit.
1. Dynamic Circuit
4.2 equation and initial conditions of dynamic circuit
When the dynamic circuit state changes, it needs to go through a change process to reach a new stable state. This change process is called the transient process of the circuit.
A change in the structure or state of a circuit
Switching
Branch access or disconnection
Change of circuit parameters
Causes of the transient process
There are energy storage elements in the circuit, the energy changes when the circuit changes, and the energy storage and release need a certain time to complete

## Slide 21
Applying KVL and VCR
the current as the variable：
+
–
uC
us（t）
R
C
i
(t >0)
2. Equations of dynamic circuit

## Slide 22
+
–
uL
us（t）
R
L
i
(t >0)
active
resistor
circuit
Dynamic
element
First-order circuit
Applying KVL and VCR
inductor voltage is variable：

## Slide 23
+
–
uL
uS（t）
R
L
i
(t >0)
C
uC
＋
－
＋
－
Second-order circuit
current as variable：

## Slide 24
First-order circuit
There is only one dynamic element, and the expression describing the circuit is a first-order linear differential equation.
（1）The circuit equations describing dynamic circuits are differential equations;
Conclusion：
（2）The order of dynamic circuit equation is equal to
the number of dynamic elements in the circuit.
Second-order circuit
There are two dynamic elements, and the expression describing the circuit is a second- order linear differential equation.

## Slide 25
(1) t = 0+ and t = 0-
Suppose that at t = 0, the circuit switches.
0- : the time just before t=0
0+ : the time just after t=0
3. Initial condition
The initial conditions are the values of u, i and their derivatives when t = 0+.
0-
0+
0
t
f(t)

## Slide 26
When t = 0+
i() is finite,
i
uc
C
+
-
q (0+) = q (0-)
uC (0+) = uC (0-)
At the moment of circuit changing, if the current of the capacitor was limited, the capacitor voltage (or charge) remains constant before and after the circuit switching.
(2) Initial condition for C
0
q =C uC
Conclusion

## Slide 27
u is finite,
L (0+)= L (0-)
iL(0+)= iL(0-)
i
u
L
+
-
L
(3) Initial condition for L
When t = 0+
0
At the moment of circuit changing, if the voltage of inductor is finite, the current (or flux linkage) of inductor remains constant before and after the circuit changing.
Conclusion

## Slide 28
L (0+)= L (0-)
iL(0+)= iL(0-)
q (0+) = q (0-)
uC (0+) = uC (0-)
(4) Switch Law
（1）The conditions of Switch Law are that capacitor
current and inductor voltage are finite value.
Note:
At the moment of circuit switching, if the voltage of inductor is finite, the current (or flux linkage) of inductor remains constant before and after the circuit switching.
At the moment of circuit switching, if the current of the capacitor was limited, the capacitor voltage (or charge) remains constant before and after the circuit switching.
（2）Switch law reflects that energy cannot change abruply.

## Slide 29
(5) initial values
(2) According to Switch Law
uC (0+) = uC (0-)=8V
+
-
10V
i
iC
+
8V
-
10k
0+
the equivalent circuit
(1) Find uC(0-) and iL(0-) from the circuit at t= 0-.
+
-
10V
+
uC
-
10k
40k
uC(0-)=8V
(3) Find iC(0+) from the equivalent circuit when t=0+.
iC(0-)=0 iC(0+)
Example 1
Find iC(0+)
+
-
10V
i
iC
+
uC
-
k
10k
40k
open circuit
capacitor is replaced by a voltage source

## Slide 30

iL(0+)= iL(0-) =2A
Example 2
When t = 0, close the switch K. Find uL(0+).
iL
+
uL
-
L
10V
K
1
4
+
uL
-
10V
1
4
the equivalent circuit at t=0+
2A
Find
From Switch Law:
Inductor is replaced by current source
Solution:
iL
short circuit
10V
1
4

## Slide 31
Steps to find initial values:
1. Firstly, find uC(0-) and iL(0-) ;
2. Secondly, find uC(0+) and iL(0+) by Switch Law;
3. Draw equivalent circuit at t=0+ .
4. The value of each variable at t =0+ can be obtained from the equivalent circuit at t=0+.
b. The capacitor (inductor) is replaced by a voltage source (current source).
a. This is a circuit after switching.

## Slide 32
iL(0+) = iL(0-) = IS
uC(0+) = uC(0-) = RIS
uL(0+)= - RIS
Find iC(0+) , uL(0+)
Example 3
K(t=0)
+
–
uL
iL
C
+
–
uC
L
R
IS
iC
Solution:
the equivalent circuit at t=0+
uL
+
–
iC
R
IS
R IS
+
–
R
IS
the equivalent circuit at t=0-

## Slide 33
Example 4
iL
+
uL
-
L
K
2
+
-
48V
3
2
C
Calculate the branch current and inductor voltage at the moment when switch K is closed.
Solution:
the equivalent circuit at t=0-
12A
24V
+
-
48V
3
2
+
-
i
iC
+
-
uL
the equivalent circuit at t=0+
iL
2
+
-
48V
3
2
+
－
uC

## Slide 34
Example 5
Find the current flowing through switch K
at the moment when it is closed.
iL
+
200V
-
L
K
100
+
uC
100
100
C
－
Solution:
（1）Find 0-:
（2）Find 0+ circuit:
1A
+
200V
-
100
+
100V
100
100
－
+
uL
－
iC
uC(0+) = uC(0-) = 100V

## Slide 35
4.3 Zero-input response of first-order circuit
Zero-input response refers to the response caused by the initial energy storage of energy storage element (dynamic element) without external excitation.
1.Zero-input response of RC circuit
uC (0-)=U0
Characteristic
Root:
Characteristic
Equation:
RCp+1=0
uR= Ri
Zero-input response
i
K(t=0)
+
–
uR
C
+
–
uC
R

## Slide 36
uC (0+)=uC(0-)=U0
A=U0
or

## Slide 37
t
U0
uC
0
I0
t
i
0
（1） The voltage and current are the functions that decay with time according to the same exponential law;
Conclusion：
continuous function
jump
（2） The response is linear with the initial state, and its decay rate is related to RC.
 =RC.  is called time constant of First-order circuit.
unit

## Slide 38
The time constant  reflects the transition time of the circuit.
 = R C
The larger is, the longer the transition time is.
The smaller is, the shorter the transition time is.
When the initial voltage is constant,
R is larger ( C is constant）,
discharge current i=u/R is smaller
 is large and
discharge time is longer
U0
t
uc
0
 is small
 is big
C is larger（R is constant）,
initial energe w=Cu2/2 is larger
physical meanings

## Slide 39
：The time required for the capacitor voltage to decay to 36.8% of original voltage.
＝ t2－t1
The slope of the curve at time t1 is :
I0
t
uc
0

t1
t2
U0 0.368 U0 0.135 U0 0.05 U0 0.007 U0
t
0  2 3 5
U0 U0 e -1 U0 e -2 U0 e -3 U0 e -5
It is considered that the transition process will be completed after 3－5.
subtangent

## Slide 40
（3）Energy
The capacitor releases energy continuously and is absorbed by the resistor until it is completely consumed.
Assume uC(0+)=U0
Capacitor releases power：
Resistor absorbed power：
uC
R
+
－
C
i

## Slide 41
Example
The capacitor in the circuit is originally charged with a voltage of 24V. Find the capacitor voltage and the current of each branch after switch K is closed.
Solution:
This is a zero-input response problem of RC circuit,
i3
K
3
+
uC
2
6
5F
－
i2
i1
+
uC
4
5F
－
i1
t >0
equivalent circuit
Substitute

## Slide 42
2.Zero-input response of the RL circuit
Characteristic Equation: Lp+R=0
Characteristic Root:
Substitute initial value: i(0+)= I0
A= i(0+)= I0
i
K(t=0)
US
L
+
–
uL
R
R1
t >0
i
L
+
–
uL
R
We have:

## Slide 43
-RI0
uL
t
t
I0
iL
0
Conclusion：
continuous function
jump
（1） The voltage and current are the functions that decay with time according to the same exponential law;
（2）The response has a linear relationship with the initial
state, and the attenuation speed is related to L/R.

## Slide 44
 = L/R is called time constant of RL circuit.
L is larger, initial energy w=Li2/2 is larger;
R is smaller, p=Ri2 is smaller, so
discharge process consumes little energy.
 is large and discharge time is longer.
Physical meanings
 = L/R
The initial value of current i(0) is constant：
H
Ω
Wb
A·Ω
V·S
A·Ω
S
The time constant  reflects the transition time of the circuit.
The larger is, the longer the transition time is.
The smaller is, the shorter the transition time is.

## Slide 45
（3）Energy
The inductor releases energy continuously and is absorbed by the resistor until it is completely consumed
Assume iL(0+)=I0
Inductor releases energy：
Resistor absorbs energy：
i
L
+
–
uL
R

## Slide 46
iL (0+) = iL(0-) = 1 A
uV (0+)=－ 10000V causes
V
damage.
Example 1
When t=0 , switch on K and find uv. The range of voltmeter is 50V.
Solution:
iL
L
R
10V
iL
K(t=0)
+
–
uV
L=4H
R=10
V
RV
10k
10V

## Slide 47
Example 2
When t=0 , the switch K changes from 1 to 2. Find the inductor voltage, current flowing through inductor and u12.
Solution:
iL
K(t=0)
+
–
24V
6H
3
4
4
6
+
－
uL
2
1
2
t >0
i
L
+
–
uL
R

## Slide 48
Summary
4.Zero-input response of a first-order circuit is proportional to
the initial value.
The zero input response of the first-order circuit is caused by the initial value of the energy storage element, and it is an exponential decay function that the initial value decays to zero.
2. Decay speed depends on the time constant .
RC circuit  = RC , RL circuit  = L/R
R is equivalent resistance of a terminal circuit connected to a dynamic element.
3. All responses in the same circuit have the same time constant.
iL(0+)= iL(0-)
uC (0+) = uC (0-)
RC circuit
RL circuit

## Slide 49
Zero state response refers to the response of the circuit generated only by external excitation in the zero initial state (the initial energy storage of dynamic components is zero).
i
K(t=0)
US
+
–
uR
C
+
–
uC
R
uC (0-)=0
4.4 Zero-state response of first-order circuit
Non-homogeneous linear differential equation.
Solution is：
1.Zero-state response of RC circuit
Zero-state response
General solution
Special solution

## Slide 50
Solution:
uC (0+)=A+US= 0
A= － US
The constant A is determined by the initial condition uC (0+)=0.
General solution
General solution
（free coomponent，transient component）
Special solution
（force component，steady-state component）
Special solution

## Slide 51
-US
uC'
uc''
US
t
i
0
t
uc
0
（1） Voltage and current are functions that change with time according to the same exponential law;
The capacitor voltage consists of two parts:
Continuous function
jump
steady-state component
(forced component)
transient component
+

## Slide 52
（2）The speed of the response is determined by the time
constant ＝RC.
When  is large, charging is slow; when  is small, charging is fast.
（3）The response is linear to the excitation；
（4）Energy.
Energy storage：
The energy provided by a source：
The energy consumed by a resistor:
R
C
+
-
US
Half of the energy provided by the source is consumed in the resistor, and half of it is converted into electric field, and the energy is stored in the capacitor.

## Slide 53
Example:
When t=0, switch K is closed. Given uC (0 -) = 0, calculate (1) capacitor voltage and current; (2) charging time t when uC＝80V .
Solution:
500
10F
+
-
100V
K
+
－
uC
i
(1) This is a RC zero-state response problem
（2）Assume that uC＝80V after t1 seconds:

## Slide 54
2. Zero-state response of RL circuit
iL
K(t=0)
US
+
–
uR
L
+
–
uL
R
When iL(0-)=0，the equation is ：
t
uL
US
t
iL
0
0

## Slide 55
Example 1
When t=0, Switch K is opened. Find iL and uL after t>0.
Solution:
This is a RL zero-state response problem：
iL
K
+
–
uL
2H
R
80
10A
200
300
iL
+
–
uL
2H
10A
Req
t>0

## Slide 56
Example 2
When t=0 ,Switch K is opened. Find iL, uL and terminal voltage of current source afte t>0.
Solution:
This is a RL zero-state response problem：
iL
K
+
–
uL
2H
10
2A
10
5
+
–
u
t>0
iL
+
–
uL
2H
US
Req
+
－

## Slide 57
4.5 Complete-response of first-order Circuit
The response of a first-order circuit with non-zero initial state under external excitation is called complete response.
i
K(t=0)
US
+
–
uR
C
+
–
uC
R
Solution is uC(t) = uC' + uC"
uC (0－)=U0
Taking RC circuit as an example, the differential equation of the circuit is:
=RC
1. Complete Response
Complete Response
Steady-state solution :
uC'' =US
Transient solution：
uC (0+)=A+US=U0
 A=U0 - US
Assuming initial value is A

## Slide 58
2. Two decomposing ways of total response
uC"
-US
U0
Transient solution
uC'
US
Steady-state solution
U0
uc
Total solution
t
uc
0
（1）Emphasize the two working states of the circuit
Forced component
(Steady-state solution)
Free component
(Transient solution)
Total response
Forced component
(Steady-state solution)
Free component
(Transient solution)
=
+
Clear physical concept

## Slide 59
i
K(t=0)
US
+
–
uR
C
+
–
uC
R
uC (0－)=U0
i
K(t=0)
US
+
–
uR
C
+
–
uC
R
=
uC (0－)=0
+
uC (0－)=U0
C
+
–
uC
i
K(t=0)
+
–
uR
R
Total response=Zero-state response+Zero-input response
Zero-state response
Zero-input response
(2) Focus on causality--It is convenient for superposition calculation.

## Slide 60
Zero-state response
Zero-input response
t
uc
0
US
Zero-state response
Total response
Zero-input response
U0

## Slide 61
Example 1
When t=0,Switch K is opened. Find iL and uL after t>0.
Solution:
This is an RL circuit complete response problem：
iL
K(t=0)
+
–
24V
0.6H
4
+
－
uL
8
Zero-input response：
Zero-state response：
Total response：

## Slide 62
find Steady-state component：
Total response：
Substitute initial value,we have:
6＝2＋A
A=4
iL
K(t=0)
+
–
24V
0.6H
4
+
－
uL
8
Total response：

## Slide 63
Example 2
When t=0, Switch K is closed. Find iC, uC and terminal voltage of current source after t>0.
Solution:
This is an RC circuit Total response problem：
+
–
10V
1A
1
+
－
uC
1
+
－
u
1
Steady-state component：
Total response：
A=－10

## Slide 64
3. Three-element method for first-order circuit
The mathematical model of a first-order circuit
is a first-order differential equation：
t = 0+
The general form of the solution is:
Applying 0+ equalation circuit
Applying t→ Steady-state circuit
Excitation is DC：
τC=RC, τL=L/C
The analysis of the first-order circuit problem is transformed into the problem of solving the three elements of the circuit.

## Slide 65
1A
2
Example 1
1
3F
+
-
uC
When t=0, switch is closed. Find uC(t) after switching circuit.
Solution:
t
uc
2
(V)
0.667
0

## Slide 66
Example 2
When t=0 , switch is closed. Find iL, i1 and i2 after t>0.
Solution:
The three-element is：
iL
+
–
20V
0.5H
5
5
+
–
10V
i2
i1

## Slide 67
The three elements are：
+
–
20V
2A
5
5
+
–
10V
i2
i1
0＋ equivalent circuit

## Slide 68
Example 3
When t=0, switch from 1→2. Find uC(t) after switching circuit.
2A
4
1
0.1F
+
uC
－
+
－
4
i1
2i1
8V
+
－
1
2
Solution:
The three elements are：
4
+
－
4
i1
2i1
u
+
－

## Slide 69
Example 4
When t=0 switch is closed. Find i(t) after switching circuit.
Solution:
The Three-element is：
+
–
1H
0.25F
5
2
S
10V
i

## Slide 70
4.6 Step Response of First-Order Circuit
The zero-state response of the circuit to the unit step function is called the unit step response.
1. Unit Step
function
1. Singularity function
Unit Step Response
2. Delay unit step function
3. Delay step function：A(t-)。
Step function starting at time :(t-)

## Slide 71
1. Represent the state of the switch
2. Function of step function
2. Unit step function is used to "start" any function f(t).
3. Represent a staircase wave.
uC(0-)=0
f（t）(t)：start a function by (t).

## Slide 72
Example：In the circuit shown in Figure (a), the circuit has reached a stable state when the switch S is closed at 1. When t = 0, the switch turns from 1 to 2, and when t =  =RC, it turns from 2 to 1. Find the uC(t) when t≥0.
When t > ,circuit is shown in Figure(c)
When 0≤t< ,circuit is shown in Figure(b).
Figure(a)
Figure(b)
Figure(c)
Solution 1：

## Slide 73
Solution 2:
The excitation is divided into the superposition
of two step sources.
The voltage of capacitor can be regarded as two zero-state
equations, but the starting time is different，so we have:

## Slide 74
4.7 Impulse response of first-order circuit
The zero-state response of the circuit to the unit impulse function is called the unit impulse response.
1. Unit Impulse function
1. Impulse function
Unit Impulse Response
2. Delay Impulse function
Delay Impulse functionk(t-2)
Impulse intensity is k
Delay Impulse function (t-1)
Unit Impulse function (t)
Impulse intensity is 1

## Slide 75
1.Integration of unit impulse functon (t)to time is equal to unit step function (t):
2. The nature of the impulse function
Conversely, the first derivative of the step function (t)to time is equal to the impulse function (t):
2.For any function f(t) that is continuous at t = 0,
there will be:
Thus:

## Slide 76
When excitation is 10(t).
step response
impulse response
Example 1: Circuit is shown in
figure，Find i (t).
Solution：When excitation is ε(t).

## Slide 77
2、Find Impulse response h(t)
Solution：
1、Find Step response S(t)
Example 2：Find Impulse response i.

## Slide 78
Homework： 4-21，22，26，30，31， 34，35，39，43，44